## Slide 1
How to create an AND logic circuit using the Arduino UNO microcontroller?

## Slide 2
and an Integrated Development Environment (IDE) software to write the MCU control code in a simplified version of C++, then compile and upload the code to the board.
Arduino is an open-source platform for building electronics projects. It consists of an open source hardware called Arduino board

## Slide 3
TINA and TINACloud provide an extensive support for Arduino.
You can simulate, debug and bring your design to life in a mixed circuit environment before uploading it to the board.

## Slide 4
Now let's see the steps of creating an AND logic circuit using the Arduino UNO microcontroller.
First download & install the latest Arduino program from the Arduino website:
https://www.arduino.cc/en/Main/Software

## Slide 5
Set the Arduino path in TINA as follows before using Arduino for the first time.
Click on the Analysis menu on the Toolbar &
Select Options...

## Slide 6
Press the Advanced... Button in the Analysis Options Window

## Slide 7
Next, click the "Select Arduino path" button in the
Advanced Options Window

## Slide 8
and select Arduino
(in our case: C:\Program Files (x86)\Arduino)
Press the OK button

## Slide 9
Press OK again to close the Advanced Options Display window

## Slide 10
Now click OK to close the Analysis Options Window

## Slide 11
Now lets create a new schematic diagram.
Click the File menu then select New

## Slide 12
Select the “Insert” menu.
Select Macro...

## Slide 13
Select the Macrolib folder of TINA and double-click the Arduino folder

## Slide 14
Open the Arduino Uno.TSM

## Slide 15
The Macro will be attached to your cursor, you can place it wherever you wish on the workspace.

## Slide 16
Let’s create the following circuit:

## Slide 17
Select a “Voltage Source” from the “Basic” Toolbar and place it on the workspace.

## Slide 18
Set its “Voltage” parameter to 5V.

## Slide 19
Select and place a Ground from the “Basic” Toolbar.

## Slide 20
Next, select and place 3 Resistors

## Slide 21
Double-click the Resistors and set their
“Resistance” values to 220, 10K and 10K.

## Slide 22
Select and place an “LED” from the “Semiconductors” Toolbar.

## Slide 23
Select and place 2 Switches from the “Switches” Toolbar.

## Slide 24
Select and place 4 Jumpers from the “Special” Toolbar

## Slide 25
and change their labels to 5V.

## Slide 26
then select and place 5 more jumpers & change their labels to GND.

## Slide 27
Finally connect the components.

## Slide 28
Load the controlling program into the microcontroller
Double-click on the Arduino UNO, then press the “Enter Macro” button.

## Slide 29
The ATMEGA328P MCU used in Aurdino UNO appears

## Slide 30
Click the 3 dots button in the “C-code” field

## Slide 31
Next, click the “C Code” in the MCU Input File Selection window

## Slide 32
Click the “Project” button in the MCU IDE window and select Compiler Options.

## Slide 33
In the C Compiler Settings window make sure Arduino....is selected.
then Click OK

## Slide 34
Click the "Add existing file to Project" icon in the MCU IDE window.

## Slide 35
Select the AND_gate.ino file, then click Open.

## Slide 36
Next click on the "Make Project" button.

## Slide 37
When the "Compile succesful" message appears,
press the "Save Project" button.
Close the MCU IDE window,

## Slide 38
then press “OK” to close the MCU Input File Selection window as well.

## Slide 39
Click OK to close the “Enter Macro”window.

## Slide 40
Finally press the “TR” button to start the Interactive Simulation.
Click the left (SPST3) and right (SPST4) switches to close both switches.

## Slide 41
When both switches are closed, the LED lights up.

## Slide 42
www.tina.com
For more information visit our website at
www.tinacloud.com
https://www.youtube.com/user/TinaDesignSuite
Visit our YouTube channel at